## Slide 1: NAO
Getting started
21-08-2019
Richard van Santen

## Slide 2: What’s in the box?
01

## Slide 3: Installation
NAO (password: altran2018)
WIFI Accesspoint + Adapter (router admin password: altran2018)
Charger for NAO
Additional battery for NAO

## Slide 4: NAO Overview
Microphone 4 directional
Speakers 4 directional
Camera 1280*960@30fps 2x
Sonar 2x
IR Leds 2x
Internet: Wifi / Ethernet
USB for connecting e.g. Arduino board for additional sensors
19 languages for recognition and text to speech
ATOM Z530 1.6GHz CPU, 1 GB
60min of active use (5h charging)
Easy programming with Choregraphe
Development on Windows, Mac and Linux
Develop in C++, Python, .NET, Java, MatLab and Urbi

## Slide 5: Start Learning with NAO
01
What is in the box?
02
Installation
03
Start using the tooling
04
Download links

## Slide 6: Installation
02

## Slide 7: Installation
Install Choregraphe Suite 2.1.4
  Available for Windows, Linux and Mac
  When asked use this key: 654e-4564-153c-6518-2f44-7562-206e-4c60-5f47-5f45
To connect to NAO make sure you are connected to the same wifi as NAO. The wifi accesspoint is also in the case with NAO. The password of the WIFI is on the bottom of the AP.
After powering up NAO (by pressing and hold his chest button) you can press the power button on his chest once, this will let NAO tell his / her IP address.
This IP can be used to connect to NAO from the Chroregraphe software.
  NOTE: Normally the software will also start a virtual robot to test with (except audio)

## Slide 8: Naoqi-bin
Standalone simulator
Can connect the Choregraphe to this simulator
Can connect Python SDK to this simulator
  Use docker container provided in repo or: docker run -it –rm rvsanten/naopy

## Slide 9: Appendix: Choregraphe 2.1.4
After startup it will automatically connect to the virtual robot
Edit  Preferences to e.g. change virtual robot type and reduce motor speed

## Slide 10: How-to start using the tooling
03

## Slide 11: Links
04

## Slide 12: Appendix: Download Links
URL | Info
https://community.ald.softbankrobotics.com/en/resources/software/language/en-gb/robot/nao-2 | Nao downloads (account required)
https://community.ald.softbankrobotics.com/en/resources/software/former-nao-versions-choregraphe-suite | Choregraph download if needed

## Slide 13: Additional Reading
https://en.wikipedia.org/wiki/Nao_(robot)
https://www.ald.softbankrobotics.com/en/robots/nao/find-out-more-about-nao
https://developer.softbankrobotics.com/
https://developer.softbankrobotics.com/us-en/downloads/nao-v5-v4
https://stackoverflow.com/questions/tagged/choregraphe+pepper+nao-robot
https://developer.softbankrobotics.com/us-en/documents/developing-our-robots
http://doc.aldebaran.com/2-5/index.html
http://doc.aldebaran.com/2-1/family/robots/connectivity_nao.html
http://doc.aldebaran.com/1-14/family/robots/languages.html
http://www.acapela-group.com/
https://robotdiscounter.com/catalogsearch/result/?q=nao
https://developer.softbankrobotics.com/us-en/downloads/nao-v5-v4
https://youtu.be/fUyU3lKzoio
https://www.youtube.com/watch?v=wNkAr9bRJ1w
https://www.youtube.com/watch?v=2laujomh0JY
Arduino
http://www.youtube.com/watch?v=hf_6SNGZyXQ
https://www.youtube.com/watch?v=57Z4vLBgynI
https://www.youtube.com/watch?v=qghOyez6PRA